## Slide 1: AUTOMATIC PARKING COUNTER
"Navigating the Future of Parking Management"

## Slide 2: TABLE OF CONTENTS 03 04 01 02
OUR SOLUTION
Our solution and prototype to solve the parking problem
INTRODUCTION
THE PROBLEM
The current issue with parking systems.
A Project Introduction with its Real life Problem
COMPONENTS USED
Different Components required to Build these Project

## Slide 3: TABLE OF CONTENTS 07 08 05 06
PROJECT DESIGN
A Conceptual explanation of Project Idea
SOFTWARE LAYOUT
Systematic Design to
Handle different situation
FUTURE ENHANCEMENTS
Ideas to Enhance and Develop the current Project to its pros
CONCLUSION
Concluding the Project How useful its was.

## Slide 4: INTRODUCTION 01
"Join Us on a Journey to Effortless Parking“

## Slide 5: INTRODUCTION
Imagine a world where finding a parking space is no longer a hassle, where parking lots are efficiently managed, and drivers experience a seamless entry and exit process.
Our project aims to bring this vision to life by introducing a state-of-the-art solution that combines technology and automation to revolutionize the way we manage parking facilities.

## Slide 6: THE PROBLEM
Nowadays, Parking systems are dependent on human intervention or staff-maintained databases.
This leaves room for human error and can lead to mismanagement and chaos in the parking lot.
The overestimation of available parking spaces can cause overcrowding, vehicle damage or unnecessary conflict.

## Slide 7: OUR SOLUTION

## Slide 8: COMPONENTS USED 04
"Powering Efficiency, One Component at a Time"

## Slide 9: COMPONENTS USED ARDUINO UNO HC-SR04 SERVO MOTOR
A
Microcontroller Board
A
Ultrasonic Sensor Module
An Angular Positioning Motor

## Slide 10: COMPONENTS USED JUMPER WIRE BREAD BOARD LED
A Connecting Wire
A Prototyping Board
A Light Indicator

## Slide 11: PROJECT DESIGN 05
"Where Innovation Meets Infrastructure"

## Slide 12: PROJECT DESIGN CAR DETECTION GATE CONTROL CAR COUNTING LED INDICATORS
Ultrasonic sensors detect car presence at the front and rear.
The gate opens if the front sensor detects a car and parking slots are available; it closes after a brief delay.
The system tracks car count, incrementing when a car enters and decrementing when it exits.
LEDs represent parking spaces; they light up or turn off as cars enter or exit.

## Slide 13: CIRCUIT DIAGRAM

## Slide 15: SOFTWARE LAYOUT 06
"Code, Control, and Convenience"

## Slide 16: SOFTWARE LAYOUT
#include <Servo.h>
Servo gateServo; // Define a servo object for the gate
const int trigFrontPin = 2;
const int echoFrontPin = 3;
const int trigRearPin = 4;
const int echoRearPin = 5;
const int gateOpenAngle = 90; // Angle to open the gate
const int gateClosedAngle = 0; // Angle to close the gate
const int numberOfSlots = 5;
int availableSlots = numberOfSlots;
const int ledPins[] = {6, 7, 8, 9, 10};
int carCount = 0; // Initialize car count
void setup() {
gateServo.attach(11); // Servo motor control pin
pinMode(trigFrontPin, OUTPUT);
pinMode(echoFrontPin, INPUT);
pinMode(trigRearPin, OUTPUT);
pinMode(echoRearPin, INPUT);}

## Slide 17: SOFTWARE LAYOUT
for (int i = 0; i < numberOfSlots; i++) {
pinMode(ledPins[i], OUTPUT);
}
updateLEDs();
Serial.begin(9600);
void loop() {
long frontDistance = measureDistance(trigFrontPin, echoFrontPin);
long rearDistance = measureDistance(trigRearPin, echoRearPin);
// Check if a car is entering from the front
if (frontDistance < 5) {
if (availableSlots > 0) {
openGate();
availableSlots--;
carCount++;
updateLEDs();
delay(2000); // Allow 3 seconds for a car to pass through
closeGate();} }

## Slide 18: SOFTWARE LAYOUT
// Check if a car is leaving from the rear
if (rearDistance < 5) {
if (availableSlots > -1){
availableSlots++;
carCount--;
updateLEDs();
openGate();
delay(3000);
closeGate();} // Delay to prevent multiple counts for the same car
}
// Display information on Serial Monitor
Serial.print("Front Distance: ");
Serial.print(frontDistance);
Serial.print(" cm | Rear Distance: ");
Serial.print(rearDistance);
Serial.print(" cm | Available Slots: ");
Serial.print(availableSlots);
Serial.print(" | Car Count: ");
Serial.println(carCount);
}

## Slide 19: SOFTWARE LAYOUT
long measureDistance(int trigPin, int echoPin) {
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW); return pulseIn(echoPin, HIGH) / 58.2; // Calculate distance in centimeters
}
void openGate() {
gateServo.write(gateOpenAngle);
}
void closeGate() {
gateServo.write(gateClosedAngle);
}
void updateLEDs()
{// LED control logic based on available slots}
}

## Slide 20: FUTURE ENHANCEMENT 07
"Tomorrow's Parking, Today's Innovations"

## Slide 21: FUTURE STRATEGY Predictive Analytics IoT and Smart Sensors
Embrace IoT by deploying smart sensors throughout the parking area.
Collect data on vehicle types, temperature, and air quality for improved security, comfort.
Integrate data analytics and machine learning to predict parking demand.
Develop algorithms that anticipate peak hours, special events, and holidays to optimize resource allocation.

## Slide 22: FUTURE ENHANCEMENT LICENSE PLATE RECOGONITION RESERVATION SYSTEM VEHICLE CLASSIFICATION INTEGRATE WITH APPS
Implement sensors and algorithms for classifying vehicles
Recognize log license plates of entering and exiting vehicles.
Enable users to choose preferred parking locations and time slots
Real-time notifications about parking space availability and access.

## Slide 23: CONCLUSION

## Slide 24: THANK YOU!